## Slide 1: Scientific CCD Development at MIT Lincoln Laboratory
Christopher Leitz
christopher.leitz@ll.mit.edu
29 June 2022
DISTRIBUTION STATEMENT A. Approved for public release. Distribution is unlimited.
This material is based upon work supported under Air Force Contract No. FA8702-15-D-0001. Any opinions, findings, conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the U.S. Air Force.
© 2022 Massachusetts Institute of Technology.
Delivered to the U.S. Government with Unlimited Rights, as defined in DFARS Part 252.227-7013 or 7014 (Feb 2014). Notwithstanding any copyright notice, U.S. Government rights in this work are defined by DFARS 252.227-7013 or DFARS 252.227-7014 as detailed above. Use of this work other than as specifically authorized by the U.S. Government may violate any copyrights that exist in this work.

## Slide 2: MIT Lincoln Laboratory DoD Federally Funded Research and Development Center
System architecture engineering
Technology in Support of National Security
Long-term technology development
System prototyping and demonstration
Air, Missile, and
Maritime Defense
Technology
Homeland
Protection
Air Traffic
Control
Communication
Systems
Advanced
Technology
Space
Systems and
Technology
ISR Systems
and Technology
Tactical
Systems
Cyber Security
FY21 Funding: $1.185B
Headcount: 4080
Biotechnology
and Human
Systems
Engineering
~600 Active Programs
Massachusetts Institute of Technology
MIT Lincoln Laboratory, Lexington, Massachusetts
Notes: 2

## Slide 3: Advanced Imager Technology Group
Read-Out Circuits
Perceive the Hidden
Envision the Future
Developing innovative imaging and sensing technology to enable impactful National Security capabilities and scientific discovery
Instruments enabling new scientific discovery & DoD capabilities
Charge-coupled devices (CCDs)
Geiger-mode APDs
Superconducting detectors
Digital focal planes
Reconfigurable imagers
Detectors
Imaging & Sensing Applications
Today’s Focus

## Slide 4: Outline
Background and highlights of Lincoln’s scientific CCDs
Basics of CCD technology
Future directions

## Slide 5: CCDs Have Enabled Unique Capabilities in Support of National Security and Science
National Ignition Facility (LLNL)
Nuclear Stockpile Stewardship (LANL)
AMOS (USAF)
Space Surveillance
Astronomy & Near Earth Object Detection
Directed Energy
AFRL SOR
Space-Based Astronomy (Astrophysics, Exoplanet Detection, Asteroid Exploration)

## Slide 6: Astrophysics Light Sources
Figure modified from Astro2020 Public Briefing
Log(frequency) (Hz)
19
9
10
11
12
13
14
15
16
17
18
Wavelength
100 µm
1 µm
10 nm
0.1 nm
10 mm
Radio
Sub-mm
Infrared
Opt
UV
Hard X-ray
Soft X-ray
SPACE REQUIRED
SPACE REQUIRED
Mechanical AGN
Feedback
Molecular Gas, Dust
Obscured Star Formation
Obscured AGN
Star Formation
Old Stars
Lyman-alpha
Emission
X-ray Binaries
CGM, IGM, & ICM
AGN
Supernovae
Wide diversity of sources and therefore many different detector technologies needed
Capable of being detected with CCDs

## Slide 7: Space vs. Ground Observatories
Ground observatories have obvious advantages, however:
  The atmosphere is opaque in scientifically important wavebands (e.g. X-ray, infrared)
  Atmospheric turbulence degrades image quality
  There are a finite number of prime viewing sites, most in remote locations
Both ground and space-based telescopes have been steadily increasing in size
  See fainter objects at higher resolution
  Cost and complexity increase faster than telescope size
Image credit: Wikipedia

## Slide 8: Chandra X-Ray Observatory
Bullet Cluster
Mushotsky et al., (SAO)
Chandra (1999)
Supermassive Black Holes Drive Jets at Light Speed
Dark Matter Detection from Galaxy Cluster Collision
CCD focal-plane array (MITLL)
MIT High Energy X-Ray Grating

## Slide 9: Chandra in the News
August 8, 2019
August 25, 2021
Source: NASA
Chandra is still the pre-eminent X-ray observatory, 23 years after launch

## Slide 10: (Still the) World’s Largest Imager of the Night Sky
Image credit: Photograph by Rob Ratkowski for the PS1SC
Pan-STARRS Telescope
PS1 (2007)
Pan-STARRS Imager
1.4 Gigapixel imager, 10 million times more sensitive than human eye

## Slide 11: Pan-STARRS Medium Deep Field
Moon for scale
NGC 4258,
23 million light years away

## Slide 12: Detecting the First Interstellar Object (‘Oumuamua)
http://www.psrd.hawaii.edu/CosmoSparks/Aug18/PSRD-interstellar-Oumuamua.pdf
https://www.ifa.hawaii.edu/info/press-releases/Oumuamua/
Artists’ Depiction

## Slide 13: Transiting Exoplanet Survey Satellite (TESS)
All-sky, two-year photometric exoplanet discovery mission
Southern Hemisphere Full Sky Mosaic
Launched 18 April 2018
Final Lunar Resonant Orbit: 30 May 2018
https://www.nasa.gov/feature/goddard/2019/nasa-s-tess-presents-panorama-of-southern-sky

## Slide 14: Planetary Transit Detection Method
Photometric precision required for transit observations of exoplanets drives instrument and orbit design

## Slide 15: What does an Earth-like Transit Look Like?
Figures from Jon M. Jenkins et al 2015 AJ 150 56, data from Kepler
Stellar type: G2, similar to the Sun
Planetary diameter: 1.6 Rearth
Period: 385 days
Orbital distance: 1.046 AU
Days (relative)

## Slide 16: Outline
Background and highlights of Lincoln’s scientific CCDs
Basics of CCD technology
Future directions

## Slide 17: Making an Imager: Light in Semiconductors
Cross-Section of Generalized Pixel Array
Semiconductors defined by an energy gap that must be overcome for an electron to move about freely
Light with energy above that energy gap can excite an electron* which can be turned to a digital signal
  Efficiency of that excitation process  quantum efficiency
Most of our scientific imagers are looking at dark scenes (“photons are currency**”), so low noise operation is critical
  Dark noise: nuisance signals, due to semiconductor material properties and defects in the material
  Read noise: the cost to measure the amount of charge in each pixel
Semiconductor
Anti-reflective coating
Photon
Pixel
* Exception to be discussed later!
** credit: Prof. Sara Seager (MIT)

## Slide 18: Semiconductor Detector Taxonomy
Serialized amplification of light-induced charge in a 2D array of capacitors
  Highly uniform response
  Excellent sensitivity
  Flight heritage
  Custom (high-voltage) electronics
  Low frame rates, less radiation hard
Charge-Coupled Devices
The technology in your cell phone: light  charge and amplified in each pixel
  High frame rates & low noise
  In-pixel processing straightforward
  Somewhat less sensitive to infrared light
  Incapable of moving charge between pixels
Active-Pixel Sensors
Specialized detector where single photon generates a massive signal
  Single photon sensitivity
  No read noise
  Excellent time resolution
  Photon detection efficiency
  Optical crosstalk, reset time
Geiger-Mode Avalanche Photodiodes

## Slide 19: Charge-Coupled Device (CCD) Operation
In a CCD, light is turned into electrons and collected within each pixel
  Each pixel is one of the terminals in a capacitor, separated from the other terminal by an insulating film
By applying time-varying voltages to these capacitors, the electrons can then be passed serially into the output
  Electrons are first quickly transferred from the imaging array pixels into a frame-store region
  Each pixel in the frame store region is transferred to the readout amplifier individually (row by row, then column by column)
Thousands of transfers, so high charge-transfer efficiency (>99.9999%) is key to CCD operation
Top-Down View of Frame-Transfer CCD Operation
Imaging Array
Frame Store
Readout Amplifier
Serial Register

## Slide 20: MIT-LL Microelectronics Laboratory An Enabling Resource for CCD Fabrication
Production-class 90-nm toolset on 200-mm diameter wafers
ISO 9001 certification, DoD trusted foundry
R&D through flight deliverables

## Slide 21: CCD Design Details
Polysilicon
SiO2 / Si3N4
(insulators)
Silicon
Capacitor Formation Process
Microscope Image of CCD Output Region
50 µm

## Slide 22: Detector Fabrication: Frontside vs. Backside Illumination
Front-Illuminated Detectors
Frontside Features
725 µm
Produces operational devices but sensitivity limited by obscuration from frontside features
Back-Illuminated Detectors
Absorbing region
Handle wafer or
readout circuit
Bonding Material
Anti-Reflective Coating
Passivation
Additional process needed for all modern scientific CCDs
Dramatically improves sensitivity
~3-250 µm

## Slide 23: Photon Absorption Length in Silicon
Chart: Photon Energy (eV)
Infrared
Ultraviolet
X-ray
Photon Wavelength (nm)
1000
100
10000
10
1
0.1
Silicon can image photons from the X-ray to near infrared
Wafer thickness
> 1 e- per photon absorbed
X-ray photons too energetic
Infrared photon energies below energy gap

## Slide 24: Silicon CCDs for X-Ray Imaging and Spectroscopy
X-ray are absorbed in silicon by imparting their energy to inner-shell electrons
  Creates a cascade event by exciting nearby outer-shell electrons
  End result is a charge “cloud” with the number of electrons directly proportional to X-ray energy
The process is not completely deterministic
  Variation in number of electrons generated depends on material properties and detector noise
  Lower variation desirable to discriminate nearby X-ray energies
X-rays also provide a valuable means of sensor calibration
Counts
104
102
100
103
101
4000
2000
0
12
6
8
2
4
10
ADU × 103
Example of X-Ray Energy Discrimination
Energy (eV)
6000
M. Bautz, et al., JATIS 5(2) 2019.
The ability to simultaneously measure position and “color” of each X-ray is a critical feature of silicon CCDs

## Slide 25: Outline
Background and highlights of Lincoln’s scientific CCDs
Basics of CCD technology
Future directions

## Slide 26: Roadmap for Next-Generation CCD Capabilities
Novel Low-Noise Amplifiers
New readout amplifier for single-photon sensitivity
Future devices will combine best features of APS and CCD imagers, supporting low-noise, high-speed imaging
High-Speed Focal Planes
Chip stacking to enable high-speed imaging, on-chip processing
Hybrid CCD-CMOS Imager
Low-Voltage CCDs
CCD operation at 2V
New process to enable lower power operation

## Slide 27: Lynx X-Ray Observatory Concept
XGS Detector Array
Lynx X-ray Microcalorimeter (LXM)
High Definition X-ray Imager (HDXI)
X-ray Mirror Assembly
Insertable Grating Arrays for X-Ray Grating Spectrometer (XGS)

## Slide 28: Lynx X-Ray Observatory Concept
XGS Detector Array
Lynx X-ray Microcalorimeter (LXM)
High Definition X-ray Imager (HDXI)
X-ray Mirror Assembly
Insertable Grating Arrays for X-Ray Grating Spectrometer (XGS)

## Slide 29: CCD Development for Lynx
Developing new CCDs to meet demanding speed, noise, and power requirements of future X-ray observatories
Collaboration with MIT Kavli Institute to develop even more capable silicon CCDs for Lynx
Parameter | Chandra | Lynx Requirement
Format | 1 Mpix | ~16 MPix
Spectral resolution @ 1 keV | > 100 eV | < 70 eV
Frame rate | 0.3 fps | 100 fps
Pixel dimensions (L × W × H) | 24 × 24 × 45 µm | 16 × 16 × 100 µm

## Slide 30: Opportunity for Large-Format, Broadband Imaging with Germanium
Chart: Photon Energy (keV)
Si (50 µm)
Ge (50 µm)
Ge (625 µm)
Chart: Wavelength (nm)
| 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800
Ge | 0.285 | 0.5 | 0.585 | 0.66 | 0.74 | 0.825 | 0.86 | 0.87 | 0.87625 | 0.8875 | 0.88625 | 0.88625 | 0.8825 | 0.88 | 0.87 | 0.8675 | 0.86 | 0.84875 | 0.835 | 0.835 | 0.83 | 0.81 | 0.805 | 0.73 | 0.50433 | 0.15131 | 0.079469 | 0.043718 | 0.019253
Si | 0.22 | 0.315 | 0.45 | 0.58 | 0.845 | 0.89 | 0.9 | 0.92 | 0.94 | 0.96 | 0.95 | 0.9 | 0.79 | 0.62 | 0.35 | 0.15
InGaAs | 0.020732 | 0.041463 | 0.072561 | 0.25915 | 0.51829 | 0.61159 | 0.70488 | 0.75671 | 0.79817 | 0.8189 | 0.82927 | 0.83963 | 0.85 | 0.85 | 0.83963 | 0.83445 | 0.82927 | 0.8189 | 0.79817 | 0.76707 | 0.51829 | 0.10366 | 0.057012 | 0.020732 | 0.010366
Si
Ge
InGaAs
Short-Wave IR
UV
VIS
Near IR
UV-SWIR
X-Ray
Monolithic & simple detector  high yield, small pixels
Advantageous material properties  low read noise
Broadband sensitivity
…in a large-format, low-noise detector

## Slide 31: Germanium CCD Development at MIT Lincoln Laboratory
8 process steps
100 µm features
1st-Generation
(Prototype) Imagers
2nd-Generation Imagers
Test Devices
75 process steps
2 µm features
180 process steps
1 µm features
280 process steps
0.2 µm features
2013
2017
2015
2020
512 x 512, 24 µm pixels
+
smaller high-speed arrays
> 300 process steps
≤ 0.2 µm features

## Slide 32: Prototype Germanium CCDs
200 µm
32 × 32 Pixel Array
Device under Test
First Light Imagery
Prototypes show expected performance, now scaling to megapixel-class imagers

## Slide 33: Lynx X-Ray Observatory Concept
XGS Detector Array
Lynx X-ray Microcalorimeter (LXM)
High Definition X-ray Imager (HDXI)
X-ray Mirror Assembly
Insertable Grating Arrays for X-Ray Grating Spectrometer (XGS)

## Slide 34: Proof-of-Concept X-ray Microcalorimeter for Lynx
Provides sensor that combines large format with high spectral resolving power
Array Size and Energy Resolution
Chart: Resolving Power (E/E)
| 10000 | 1000
 | 1 | 1
 | 64 | 256 | 1024 | 49100
 | 1000000 | 10000000
horizontal | 1 | 1 | 1 | 1 | 1
vertical | 1 | 10 | 100 | 1000 | 10000 | 100000 | 1000000 | 10000000 | 100000000
horizontal | 1 | 1 | 1 | 1 | 1
vertical | 1 | 10 | 100 | 1000 | 10000 | 100000 | 1000000 | 10000000 | 100000000
CCDs
Spectrometers
Microcalorimeters
MITLL/ GSFC
(Demo, 2018)
GSFC
(Demos, 2008 - 2015)
Lynx Goal
Lynx Goal
Lynx Goal
Chandra
Chandra
Resistance
Temperature
Lynx X-Ray Microcalorimeter Detail
Main Array
86,400 pixels, ∆E = 3 eV
Enhanced Main Array
14,400 pixels, ∆E = 2 eV
Ultra-high Resolution Array
3,600 pixels, ∆E = 0.3 eV
15 mm
Desired LXM pixel count is ~1000x higher than largest arrays flown to date

## Slide 35: Superconducting Integrated Circuit Fabrication
MITLL has established a multi-layer superconducting wiring technology
  8-inch wafers
  Fully planar process
  High-yield
Leverage existing advanced superconducting electronics process at Lincoln Laboratory to enable large-format microcalorimeters
Superconducting Integrated Circuit Cross-Section

## Slide 36: Large-Format X-ray Microcalorimeter Arrays Demonstrated with MITLL Superconducting Wiring
Prototype LXM arrays with 49,100 pixels
20 mm
Successful demonstration of prototype Lynx X-ray microcalorimeter using high density,
multi-layer Nb superconducting wiring
Chart: Year
| 2000 | 2008 | 2012 | 2016
Transition Edge Sensors | 4 | 64 | 256 | 1024
vertical | 1 | 10 | 100 | 1000 | 10000 | 100000 | 1000000
Doubling time ~ 2 years
GSFC and LL
GSFC
Half the size of the full Lynx X-ray Microcalorimeter array (49.1 kpix), 3 types of array on single focal plane
Meets challenging energy resolution for Lynx
Wiring is complete, but bond pads are only available to connect a limited number of pixels in this prototype
Microcalorimeter “Moore’s Law”

## Slide 37: 100 x 100 mm Stitched Reticle for Microcalorimeters
100x100 mm stitched reticle to create room for microwave multiplexer chip to read out all 100 kpixel microcalorimeter array with 10s of rf lines
The reticle will serve as the backplane to connect all the chips together
Lincoln wiring, when integrated with microcalorimeter array at GSFC, will retire the risk of realizing a 100 kpixel-class microcalorimeter array for Lynx
200 mm Wafer with 100 x 100 mm Stitched Reticle

## Slide 38: Summary
MIT Lincoln Laboratory develops novel imagers for a variety of DoD and scientific missions
Charge-coupled devices (CCDs) provide unparalleled size, uniformity and efficiency
  Can detect radiation ranging from soft X-ray to near infrared (4 orders of magnitude difference in wavelength)
  Future developments include high-speed CCDs for X-ray observatories and germanium imagers for hard X-ray detection
Superconducting detectors provide exquisite energy resolution to complement capabilities of CCDs

## Slide 39: Some Final Reflections
One of the best parts of working at Lincoln is the chance to develop technology that enables amazing scientific discoveries
  Instrumentation plays a pivotal role in advancing the frontiers of knowledge
  These instruments are only possible through the hard work of many very talented scientists and engineers
  Part of my job is to be a steward for this culture
The time required to take an early concept and develop it fully for future observatories is measured in decades
  I keep telling myself that!
  I hope to bounce my grandkids on my lap at a launch site some day

## Slide 40: – Thank you for your time –